## Slide 1: EE394V Project Learning for DC-OPF: Classifying active sets using neural nets
-
Park, JeeHyun
06 MAY 20

## Slide 2: Contents
This slides are about a project that is based on the content covered in “Learning for DC-OPF: Classifying active sets using neural nets” [1].
Motivation & Context
Problem Formulation
Proposed Method
Experiments and Results
Further Studies
This project can be found in the following git repository.
  https://github.com/jhyun0919/OPF_Porject_EE394V_SPR2020

## Slide 3: 1. Motivation & Context
Optimal power flow is used in power system operational planning to estimate the most economical efficiency solution while satisfying demand and safety margins.
Due to increasing uncertainty and variability in energy sources and demand, the optimal solution needs to be updated near real-time to respond to observed uncertainty realizations.
The existing method of solving the optimal problem could not cope with frequent updating due to the low computational efficiency.
 A new method is required to solve the optimal power flow problem accurately with high computational efficiency.

## Slide 4: 2. Problem Formulation
DC-OPF
  ρ(ω): Control policy
    A mapping adjusts the generation in response to uncertainty realization.
    parameter (given)
      uncertainty realization (ω)
    unknown variable (wanted)
      optimal solution (p*)

## Slide 5: 2. Problem Formulation
DC-OPF
  The feasible set (polytope) can be represented in matrix form.

## Slide 6: 2. Problem Formulation
Machine learning method (direct mapping)
  Uncertainty realization  [ML Predictor]  Optimal solution.
Ensemble control policy [6][7]
  Uncertainty realization  [Searching Algorithm]  Active constraints  Optimal solution.
  The active set approach for optimal solution relies on two observation.
    For typical uncertainty distributions of the random vector ω, only a few of the active sets are realized.
    The optimal solutions to linear programs lie at extreme points of the feasible polytope.

## Slide 7: 3. Proposed Method
 | ML method (direct mapping) | Ensemble control policy [6][7]
Advantages | High computational efficiency at inference stage. | High accuracy by identifying the relevant constraints at the optimal.
Disadvantages | Low performance when the size of training data is not large enough. | Low computational efficiency due to the exhaustive searching algorithm.
Proposed Method | Use a NNs classifier for identifying the relevant constraints at the optimal. Use a NNs classifier instead of the exhaustive searching algorithm.  High computational efficiency. Map from the uncertainty realization to the active constraints set at optimality instead of the optimal solution (direct mapping).  Guarantee the satisfactory performance.

## Slide 8: 4. Experiments and Results
NN architecture
SIGMOID
Input: xn
  Uncertainty realization.
Output: yk
  {active constraints  0 ~ 1}
  Probability for each active constraints.
Further study
  Build a set of parallel binary classifiers to predict the status of each individual constraint separately.
  It will be an approach to develop a deeper understanding of various operational patterns, such as clustering of constraints.
[Personal project]
Input: xn
  Uncertainty realization.
Output: yk
  {all active constraints  0 or 1}
  Whether constraint is active.

## Slide 9: 4. Experiments and Results
Classification performance

## Slide 10: 4. Experiments and Results
Constraints cluster visualization
  +1: active constraint
  0: inactive constraint
  -1: meaningless data (added cells to make the array as a square matrix)

## Slide 11: References
[1] D. Deka and S. Misra. “Learning for DC-OPF: Classifying active sets using neural nets,” 2019 IEEE Milan PowerTech,2019.
[2] B. Borkowska, “Probabilistic load flow,” IEEE Transactions on Power App. Syst., vol. PAS-93, no. 3, pp. 752–759, 1974.
[3] M. Vrakopoulou, K. Margellos, J. Lygeros, and G. Andersson, “Probabilistic Guarantees for the N-1 Security of Systems with Wind Power Generation,” in Probabilistic Methods Applied to Power Systems (PMAPS), Istanbul, Turkey, 2012.
[4] L. Roald, S. Misra, T. Krause, and G. Andersson, “Corrective control to handle forecast uncertainty: A chance constrained optimal power flow,” IEEE Trans. Power Systems, vol. 32, no. 2, pp. 1626–1637, 2017.
[5] L. Roald, S. Misra, M. Chertkov, and G. Andersson, “Optimal power flow with weighted chance constraints and general policies for generation control,” in IEEE Conference on Decision and Control (CDC). IEEE, 2015, pp. 6927–6933.
[6] Y. Ng, S. Misra, L. A. Roald, and S. Backhaus, “Statistical learning for DC optimal power flow,” Jan. 2018.
[7] S. Misra, L. Roald, and Y. Ng, “Learning for convex optimization,” arXiv preprint arXiv:1802.09639, 2018.